Thanks for purchasing the TurboAir duct cleaning system.

This system contains:

Foot plate storage case

Foot plate

Brass Female air QD

Watts Water removal filter

Hose storage bag

50 ft vacuum hose with cleaning nozzle

3 different bush sizes

Dust Downer attachment (only used on the vacuum hose when using with carpet cleaning equipment as a vacuum source – this turns the dust into mud so your carpet cleaning machine can deal with the dry dirt)

Optional Equipment Availible:

1 eight gallon air compressor (use turned up all the way, needs to be able to produce at least 5.6 CFM @ 90 psi.)

25 ft air line (50 ft and 100 ft available)

Air Compressor Crankcase oil (30 Wt Non-Detergent)

Small Allen Wrench to change brush sizes

Cordless drill to remove and replace vent openings

Octavac 6 Stage HEPA vacuum system.

Horse Hair Duster brush attachment.

7 ft fiberglass or metal ladder

Dust mask and eye safety glasses

ULV Fogger

Air Duct Sanitizer

Drop Cloths

Initial equipment set up:

If you are purchasing a new air compressor, be sure to add 30 weight non foaming non detergent air compressor oil to the compressor crank case.  The oil level should only be half way up the site hole.

Install the Watts water remover filter on the air compressor air outlet ball valve with the clear bowl facing down.  Make sure that the side of the Watts filter that is stamped ‘IN’ is connected to the compressor ball valve.   Install the 3/8” ID air hose to the other end of the Watts filter.  Install the female brass air quick disconnect to the end of the air hose.   Use Teflon tape or air tool thread sealant on all connections.  Be sure not to get any tape or sealant in the body of the air line for this will void your warrantee.

Make sure that you call in your air compressor warrantee to Harbor Freight tools (if purchased from us).

Follow the owner’s manual for air compressor maintenance as needed.

Basic duct cleaning procedures:
Carry 7 ft ladder (easy to move around in 8 ft ceilings) and 10 ladder (will fit inside the standard extended wheel base van) in truck as needed.
Take care of any paper work with customer.
Prep area as needed. (Move furniture to access vents, and then cover nearby furniture with plastic to protect it.) 
Turn off power to ventilation system.
After you perform your pre-inspection of the system both in the ducts and in the attic, put on your safety goggles and dust mask. Remove vent covers and place in soapy cleaner in a plastic/rubber tub.
Scrub vents with soft upholstery brush and rinse off.
Leave vent covers on driveway to dry.
Carry a couple of cans of spray paint (in different colors) as an 'add on' to repaint vents after cleaning and before installation.
Lay out and plug in all your cleaning equipment. I would leave the air compressor on the front port and just run the air hose into each room that is being cleaned.

Vacuum ventilation system intake area with duster brush attachment.
Replace and clean ventilation filter. (Great add on to sell filters)
Place magnet on AC unit to remind your customer who to call. Place plain sticker and label with date of cleaning and estimated return appointment. 
Install the appropriate size duct brush in the end of the cleaning nozzle.
Place the ladder under one of ducts/vents and hook on the air valve foot control plate.

Foot control plate will install on any rung of any metal or fiberglass ladder at any height.

If you have to use the foot plate on a hard surface, without a ladder, place plate on a scrap piece of cardboard, pad, or carpet to prevent scratching the floor.

Connect the female air hose QD and both black air hoses to the foot plate.  It does not matter which black air line goes to the right or left side of the petal.  The right side QD controls the forward spin of the brush and the second hose is the exhaust.  When you reverse the direction of the brush the right side QD then becomes the exhaust but by the time you need to reverse the brush direction.

Hook vacuum hose to your vacuum source and turn on suction.  Install dust downer in vacuum hose as need if you are using a carpet cleaning machine as a vacuum source.  If you are using a HEPA vacuum like the Octavac, no dust downer is needed.

Wear dust mask and eye safety glasses.

Install the best size brush for the duct you are cleaning.  Never try to use an oversized brush.  The best results are to use a brush that is not more than 2” larger than the duct opening.  It is better to use a brush that is too small that one that is too large.
Feed TurboAir cleaning nozzle down duct at a rate of 1" per second as far as you can.
Then reverse the direction of the brush and then pull the tool back out of the duct at 1" per second.

You do not have to turn the TurboAir off to reverse the direction of the brush.  You can toggle back and forth in directional rotation without stopping the TurboAir.
Relocate the ladder to each duct and repeat the cleaning procedure.
Clean carpet (if needed)
Change out dust mask for respirator. 
Fog with EPA approved duct sanitizer (if needed or paid for. 5 min. per duct @ 1.5 revolutions on ULV fogger) Make sure customer does not breathe atomized chemical.  We sell the supplies for fogging if needed.
Replace vent covers.
Collect. Ask customer when it would be OK to contact them for follow up appointment.

Water might collect in the Watts water filter depending on your relative humidity and temperature.  If water is seen in the clear bowl, just turn the brass knob on the bottom of the bowl to empty.  The bottom of the air compressor tank also has a drain valve.  Please make sure that you secure your air compressor to your service truck during transport.

Questions can be addressed to info@steambrite.com

Steambrite.com Supply

11104 Osgood St

San Antonio, TX 78233

210-662-9000