# IMPORTANT NOTICE

### Maintaining Your ZONTEC PA2500 and 2500H

Maintenance Kit Part# CLN25 contains all the necessary components to keep your Zontec PA2500 (including Heater models) operating at peak efficiency for the next 6 months.

This kit contains the following items:

12	part# AF4 - Air Filter

4	part# GPC46 Ceramic Generator Plate

4	part# FUS006 High Voltage Fuse

24	part# WIPE9814 Alcohol/Antistatic Wipe

To inspect and clean your ZONTEC PA2500 monthly;

- TURN THE UNIT OFF AND UNPLUG IT FROM THE POWER SOURCE.

- Remove the dirty air filters from the back of the unit.

- Using a standard Phillips #2 screwdriver, remove the 6 screws securing the cabinet cover and lift the cover off.

- Gently slide the white ceramic generator plates straight up and out of the generator frames.

- Wipe any dust from the inside of the unit with a clean dry cloth.

- Using the alcohol wipes, carefully clean each generator frame from which you pulled the ceramic generator plates.  Be sure to thoroughly clean & wipe the inside area of each generator frame at the bottom, between the 2 upright posts, where the ceramic generator plate rests.

- The alcohol wipe can also be used to clean the generator plates and remove any difficult residues, from other areas, that were not removed with the dry cloth.  The alcohol will evaporate quickly.

- Gently replace the white ceramic generator plates by sliding them straight down to the base of each generator frame.  Be sure that each ceramic generator plate slides down the 'slots' at each end and is resting on the base of the generator frame.

NOTE: Replace the old generator plates with new generator plates at each 6th month cleaning interval.

- Replace the 6 cover screws.

- Install new air filters onto the back of the machine.

- There are 3 fuse holders on the back of the machine.  The smaller fuse holders contain the 200 milliAmp high voltage fuses.  If either of these 200 milliAmp fuses is blown (NO OZONE) replace it with one of the spares supplied with this kit.  This fuse will blow if any of the ceramic generator plates is broken or if any of the generator frames becomes contaminated.  Keep your spares for future use.

- The unit is ready to be put back into service.

FOR ADDITIONAL MAINTENANCE INFORMATION CONTACT YOUR DISTRIBUTOR,

OR ZONTEC CUSTOMER SERVICE AT:

1-727-341-0547   FAX: 1-727-302-9816

Available Maintenance Supplies & Accessories	Part Number

Air Filter (6 per pack)				AF4-6PK

Alcohol Wipe (12 per pack)			WIPE9814-12PK

Fuse .200 Amp Slo-Blo (6 per pack)		FUS006-6PK

Mounting Bracket				MB1AB