IMPORTANT NOTICE

### Maintaining Your ZONTEC PA1200 and PA1200H

Maintenance Kit Part# CLN1202 contains all the necessary components to keep your Zontec PA1200 or PA1200H operating at peak efficiency for the next 6 months.

This kit contains the following items:

6	part# AF4 - Air Filters

2	part# GPC46 - Ceramic Generator Plate

2	part# FUS006 - 200 milliAmp High Voltage Fuses

12	part# WIPE9814 - Alcohol/Antistatic Wipe

To inspect and clean your Zontec PA1200 (Series II or III) monthly;

- TURN THE UNIT OFF AND UNPLUG IT FROM THE POWER SOURCE.

- Remove the dirty air filter from the back of the unit.

- Using a standard Phillips #2 screwdriver, remove the 4 screws securing the cabinet cover and lift the cover off.

- Gently slide both white ceramic generator plates straight up and out of the generator frames.

- Wipe any dust from the inside of the unit with a clean dry cloth.

- Using the alcohol wipes, carefully clean each generator frame from which you pulled the ceramic generator plates. Be sure to thoroughly clean & wipe the inside area of each generator frame at the bottom, between the 2 upright posts, where each ceramic generator plate rests.

- The alcohol wipe can also be used to clean the generator plates and remove any difficult residues, from other areas, that were not removed with the dry cloth.  The alcohol will evaporate quickly.

- Gently replace the white ceramic generator plates by sliding them straight down to the base of each generator frame.  Be sure that both ceramic generator plates slide down the 'slots' at each end and are resting on the base of the generator frames.

NOTE: Replace the old generator plates with new generator plates at each 6th month cleaning interval.

- Replace the 4 cover screws.

- Install a new air filter.  Replace this filter monthly to assist in keeping the internal components as clean as possible.

- There are 2 fuse holders on the back of the machine.  The smaller fuse holder contains the 200 milliAmp high voltage fuse.  If this 200 milliAmp fuse is blown (NO OZONE) replace it with one of the spares supplied with this kit. This fuse will blow if the ceramic generator plate is broken or if the generator frame becomes contaminated.  Keep your spares for future use.

- The unit is ready to be put back into service.

FOR ADDITIONAL MAINTENANCE INFORMATION CONTACT YOUR DISTRIBUTOR,

OR ZONTEC CUSTOMER SERVICE AT:

1-727-341-0547   FAX: 1-727-302-9816

Available Maintenance Supplies & Accessories	Part Number

Air Filter (6 per pack)				AF4-6PK

Alcohol Wipe (12 per pack)			WIPE9814-12PK

Fuse .200 Amp Slo-Blo (6 per pack)		FUS006-6PK

Generator Plate (2 per pack)			GPC46-2PK

Mounting Bracket				MB1AB